Specification: 			Model No.: SHS1206 		Solar Home Lighting Kit

Item: Solar Lighting System (3 LED lights & mobile phone charger)

Solar panel: 6W solar panel, Life Time: 10 years.

Light: 2 pieces of 12V/3W LED lights and 1 piece of 12V/1W LED bulb.

Controller: over-charging (14V) and over-discharging (10.5V) protection; short-circuit protection.

Battery: 12V - 4AH lead-acid battery (rated charging current: 1A rated discharging current: 2A)

No load loss: 8mA

USB port current: 500mA

Full charging time: 10 hours with the solar panel.

Lighting duration after fully charged: 5 hours (3 lights working at the same time)

Packaging:

1. Language: 		English.
2. Inner box size: 	390 x 235 x 220mm.
3.  Carton size:	405 x 485 x 460mm (4pcs in one carton)
4. Gross weight:	17.3KG 	Net weight: 16.4KG

Bulk Price (500+)		Small Qty. Price		Sample Price

P/A				P/A				P/A