Specification:  	Model No.: SRY-002-2

Item: SOLAR LIGHTING KIT (two lights & mobile phone charger & batteries for radio)

Solar Panel: 9V/2.5W solar panel with 5M cable, Life Time: 10 years.

Controller: over-charging and over-discharging protection; short-circuit protection.

System Battery: 5 pieces AA 1800mAH NI-MH (Nickel Metal Hydride) rechargeable batteries.

Body Material: ABS

LED Lamp: 2 pieces of 9V 18LEDs Lamp with 4M cable.

Mobile phone Battery Charger: direct mobile phone charging with several different plugs.

To charge batteries for radio/flashlight: With built-in charger to charge 2pcs included 600mAH NI-MH

Rechargeable batteries:  Take the 2pcs batteries out, after fully charged, to run your radio or flashlight.

Charging Time: approximately 6-8 hours with solar panel.

Lighting duration after fully charged:

Three mode brightness settings: On the case of 2 bulbs working at the same time: 5 hours(strong brightness), 10 hours(energy saving mode), 45 hours(low brightness)

Packaging:

1. Language: in English and Japanese (Other languages available)
2. Inner box size: 28 x 21 x 5.5cm
3. Carton size: 45 x 31 x 31cm
4. Gross weight: 12.5kg.  - net weight: 11.5kg.
5. Qty/20FCL: 7000 pieces. 	Qty/40FCL: 14000 pieces.